## Slide 1: SDN and NFV in IoT Networking
Professor D. K. Saikia

## Slide 3: Internet of Things
Billions of devices interconnected providing for new interactions between the physical world and computing, digital content, analysis, applications and services
The resulting networking paradigm is the Internet of Things (IoT)

## Slide 4: Internet of Things
Opening-up unprecedented opportunities for users, manufacturers and service providers in wide variety of sectors such as-
  Healthcare, Fitness Education, Home monitoring & automation, Agriculture, Environmental monitoring;
  Energy saving and Smart grid;
  Transportation, Inventory and production management, Security, Surveillance and many more
IoT not just links sensor devices and generates the data for a purpose, it focuses on the automation and optimization within the systems.

## Slide 5: Internet of Things
Definitions by ITU as-
IoT: The global infrastructure for the information society, enabling advanced services by interconnecting things (physical and virtual) based on existing and evolving interoperable information and communication technologies.
Thing: An object of the physical world (physical thing) or information world (virtual thing), which is capable of being identified and integrated into communication network.
Device: A piece of equipment with mandatory capabilities of communication and the optional capabilities of sensing, actuation, data capture, data storage, and data processing.

## Slide 6: IoT Structure
Service Layer:
  Provide customized services to the users. e.g. Healthcare, Smart industry, Environmental monitoring, Vehicular traffic Management etc.
Platform Layer:
  Provide platform to support and execute the IoT services.
  e.g. OS platform, Data analysis platform, Service development platform etc.
Network Layer:
  Provides connectivity for exchange of data among the devices, contents, services and users
Device Layer:
  Comprises the devices
Security:
  Security and privacy issues need to be dealt with individually at each layer
Reference: Suk Kyu Lee Et al. [7]

## Slide 7: IoT Challenges
Heterogeneity:
  Diverse forms of services dealing with data in different forms and formats and producing diverse responses
  Wide diversity of sensor, actuator devices with widely varying characteristics
  Diverse protocols and interface used in the communications and the devices
Scalability:
  Fast growing requiring addition of millions of device in short span
  Configuration and Management of vast number of devices
Agility:
  Rollout of new services with minimum delay
  Need for devices with new characteristics in short notice
Optimality:
  Sharing of resources among services for optimal use
  Share network resources, devices among services

## Slide 8: Software Defined Networking (SDN)

## Slide 9: SDN – Basic Premises
Separation of control plane and data plane
Control plane comprises the programmable controller which has the global view of the network
Data plane comprises the switches that forward the packets
Forwarding rules (flow entries) are installed at the switches by the controller

## Slide 10: Traditional Computer Networks
Data plane:
Packet streaming
  Forward, filter, buffer, mark,
  rate-limit, and measure packets
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 11: Traditional Computer Networks
  Track topology changes, compute routes, install forwarding rules
Control plane:
Distributed algorithms

## Slide 12: Software Defined Networking
API to the data plane
(e.g., OpenFlow)
Logically-centralized control
Smart,
Slow
Dumb,
Fast
Switches

## Slide 13: SDN Control and Data Planes
Control Plane:
  Logic for controlling: forwarding behavior
  Examples:
    Routing protocols, network
    Middlebox, e.g. Firewall, NAT
    Configuration
Data Plane:
  Forward traffic according to control plane logic
  Examples:
    IP forwarding
    Layer 2 switching

## Slide 14: Benefits:
Simplification of the Switch Hardware
  Faster Hardware for Higher Speed of Networking
  Lower Cost
  Commodity Hardware
  Freedom from Dependence on Vendor
Ability to deal with Heterogeneous Devices
  The code can be written to deal with devices as per need
Global View and Centralized Control
  More Efficient Control Algorithms
  Simplify Policy Enforcement
  Automate Network Configuration
  Evolution

## Slide 15: Beneficiaries:
Data centers:
  Seamless VM Migration, Layer 2/ Hybrid Routing, Efficient Traffic Engineering
  Higher Speed, Use of Commodity Hardware for lower CAPEX, OPEX
Enterprise networks:
  Not tied to a Vendor, Select Hardware based on Cost and Performance
  Fast Service Delivery
  Security Applications
Research and Innovation:
  Coexistence Innovation with Production
WANs, Wireless Networks, Cloud, IoT …

## Slide 16
SDN Architecture
Control Plane
Data Plane
SDN Controller
Application Plane
Network Applications
Security Applications
Business Applications
Southbound API (e.g., OpenFlow)
Northbound API (e.g., REST API)

## Slide 17
Southbound controllers:
  OS: NOX, POX, Floodlight, OpenDayLight, Beacon, Ryu etc.
  Protocol: OpenFlow
Northbound Controllers:
  Pyretic etc.
Available Solutions

## Slide 18: OpenFlow Controller & OpenFlow Switch

## Slide 19: OpenFlow Controller
Network OS
Controller Application
Events from switches
Topology changes,
Traffic statistics,
Arriving packets
Commands to switches
Install/ uninstall rules,
Query statistics,
Send packets

## Slide 20: OpenFlow Controller & OpenFlow Switch
OpenFlow controller communicates with switch over a secure channel
  OpenFlow protocol defines message format
OpenFlow enabled switches send the first packet of a new flow to the controller
Controller updates flow table with Packet Handling Rules

## Slide 21: OpenFlow Enabled Switch
An OpenFlow switch works with the logic-

## Slide 22: Data-Plane: Simple Packet Handling
Simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Example Rules:
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 23: Actions: Forward/Drop
Forward:
  ALL: Send out all interfaces, not including the incoming interface.
  CONTROLLER: Encapsulate and send to the controller.
  LOCAL: Send to the switch’s local networking stack.
  TABLE: Perform actions in flow table. Only for packet-out messages.
  IN PORT: Send the packet out the input port
  Optional: Normal forwarding, spanning tree
Drop:
  A flow-entry with no specified action indicates that all matching packets should be dropped.

## Slide 24: Example OpenFlow Applications
Dynamic access control
Seamless mobility/migration
Server load balancing
Network virtualization
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
NAT
Firewall
DoS attack detection etc.

## Slide 25: Dynamic Access Control
Inspect first packet of a new flow
Consult the access control policy
Install rules to block or route traffic

## Slide 26: Seamless Mobility/Migration
See host send traffic at new location
Modify rules to reroute the traffic

## Slide 27: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*
src=1*

## Slide 28: Network Virtualization
Partition the space of packet headers
Controller #1
Controller #2
Controller #3

## Slide 29: Network Function Virtualization (NFV)

## Slide 30: NFV
Virtualize Network Functions:
  Replace dedicated network appliances such as-
    Switches,
    Routers,
    Firewalls etc.
  with Software running on commercial off-the-shelf servers

## Slide 31: NFV Architecture
VNF 1
VNF 2
VNF 3
VNF n
Virtual Compute
Virtual Storage
Virtual Network
Virtualization Layer
Compute
Storage
Network
Physical Hardware Resources
Network Function Virtualization Infrastructure
Management and Orchestration

## Slide 32: NFV Architecture
  Network functions are abstracted and these are implemented in software (Virtualized Network Functions-VNF)
  VNFs are executed on VMs providing Compute, Storage and Networking services
  Physical hardware resources such as Compute Servers, Storage Devices, Networking Devices are placed under a Virtualization Layer to create the VMs
  The Management and Orchestration module manage these physical and virtual resources, compose the desired services combining the modules in appropriate sequence (Service Chaining)

## Slide 33: NFV Advantages
  Reduced Capital Expenditure
  Reduced Operating Expenditure
  Faster service rollout
    When a service is new service is required it can be formulated and composed with appropriate VNF modules and quickly rolled out
  Flexibility and Innovation

## Slide 34: SDN & NFV
  SDN and NFV can complement each other
  SDN itself can be viewed as an NFV for the control functions of the network
  SDN controller can handle the Management and Orchestration functionality of NFV
  SDN provides rapid interaction between services and infrastructures and effective control
  NFV provides Agility to Chaining of Service Functions

## Slide 35: Using SDN & NFV in IoT
  SDN and NFV can combined can be used in addressing the challenges of IoT
Heterogeneity
Scalability
Agility
Optimality
SDN
NFV
IoT Infrastructure
Rapid Interaction & Control
Agile Service Chaining

## Slide 36: Possible IoT scenario with SDN and NFV

## Slide 37: References
William Stallings, Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud”, Pearson Education, 2016
Mike Ojo et al., “A SDN-IoT Architecture with NFV Implementation”, Proc. Globecom Workshop, 4-8 Dec. 2016.
S. Bera et al., “Software-Defined Networking for Internet of Things: A Survey”, IEEE Internet of Things Journal, pp 1994-2008, Vol. 4, No. 6, December 2017.
Nikos Bizanis et al., “SDN and Virtualization Solutions for the Internet of Things: A Survey”, IEEE Access, pp 5591-5605, Vol-4, 2016.
Z. Qin et al., “A Software Defined Networking Architecture for the Internet of Things”, Proc. IEEE Network Operations and Management Symposium (NOMS), 5-9 May 2014.
A. Vahdat, M. Al-Fares, N. Farrington, R. N. Mysore, G. Porter, and S. Radhakrishnan, “Scale-out networking in the data center,” IEEE Micro, vol. 30, no. 4, pp. 29-41, Jul. 2010.
Suk K. Lee et al., “Future IoT Networks: A Survey”, Journal of Applied Sciences, October 2017.

## Slide 38: Questions?

## Slide 39: Thank You