## Slide 1: Testbed Experience for Networking Experiments and Reproducibility & Machine Learning in Communication Networks
Deep Medhi
University of Missouri – Kansas City
Joint work with Xuan Liu, Parikshit Juluri, Shuai Jack Zhao February 2018
Part of the work supported by National Science Foundation’s GENI program (GPO Contract No. 9500009441)
and NSF Grants CNS- 0916505 and CNS-1217736

## Slide 2: Experiment Challenges
Properties of the Shared Public testbed[1]
  Large scale, diverse topologies
  Resources are shared and sometimes can be limited due to high demand from other experimenters
  Relying on objective conditions, e.g., power, network connectivity, etc.
    Especially the geographical and federated testbed, e.g., GpENI, GENI, etc.
  Low-level debugging may be needed between experimenters and the testbed operators.
Challenges to the experimenters[1]
  Automation
    Easy to bring up and down the experimental
      Install necessary packages and scripts at the bootstrap stage.
    Easy to switch to another ”slice” with equivalent resources when necessary (i.e., when outage occurs)
    Execution and analytics
    Easy to scale-up the experiment, i.e., larger topologies, more nodes, more links, etc.

## Slide 3: Case Study 1 Dynamic Network Reconfiguration on the GpENI-VINI testbed[2]
GpENI-VINI testbed (starting in early round of GENI in 2008/2009)
  A geographical testbed supporting routing experiments crossing both US and Europe.
  Support arbitrary virtual topology creation and each virtual node can be configured as an virtual router (e.g., OSPF router)
(I-a) US-Europe: Five-node Topology
(II) US-Europe: Nine-node Topology

## Slide 4: Case Study 1 Dynamic Network Reconfiguration due to failure on the GpENI-VINI testbed[2]
Plan the experiment in details
  Selecting a testbed and explore the features and functionalities supported by the testbed.
    E.g., For GpENI-VINI testbed,
      Each virtual node is programmable and can be configured as a virtual router using Quagga or XORP
      Experimenters can create arbitrary virtual topologies over GpENI-VINI testbed in a programmable way.
  Selecting a proper traffic generator, and decide what to be collected
    End-to-end metrics: Throughput and bandwidth
    Network metrics: network recovery time, OSPF routing table convergence time
Systematic experimental design and execution
  Start with a small topology, and create scripts to automate the procedure
    Given a predefined topology configuration file, initializing a virtual network, along with a set of standby virtual router.
    Automate the experimental flow: failing an existing virtual router, selecting a standby virtual router, and run the reconfiguration
    Check if data and logs are collected properly.
  Repeat and Scale-up the experimental scenarios
    Create configuration file for a larger virtual topology or same topology with different set of virtual nodes, and run the automation script to execute the experimental flow
    Collect data

## Slide 5: Case Study 1 Dynamic Network Reconfiguration due to failure on the GpENI-VINI testbed[2]
Multi-run measurement results
  Next-hop information collected from the routing table over 10 runs, for two different topologies
  TCP Session bandwidth before and after the failure & reconfiguration for topology(I-a)

## Slide 6: Why the result varies from one run to another on the GpENI testbed: a brief explanation
For the next hop plots, it’s the time when a node learns it’s next hop node after the failure until the routing table get convergence. In the GpENI distributed virtualized environment, this time varies, which causes different next hop selection.
Consider Fig-4, Topology-I on slide-3:
  After the failure, from R2 TUT-FI’s perspective, it’s routing table immediately shows the neighbor was R2-simula-lo, and after about 23 second, the routing table was convergence with the standby VR R2-KU added, then it showed the time needed to update the next hop information at R2 TUT-FI was around 23 second. (please ignore the dots before 0 on the x-axis, that might because of the pre-setup of the experiments).

## Slide 7: GENI (Global Environment for Network Innovations)
GENI:
Distributed computing resources around United States
Fast Layer 2 and 3 connection ( Default 100Mbps, more can be requested in specific VLAN#)
Customization in OS and software
Resource and experiment isolation, such as running their own Layer 3 and above protocols
Notes: ref: https://www.geni.net/about-geni/what-is-geni/

## Slide 8: Pros and Cons
Pros:
A large-scale experiment infrastructure with layer 2 and layer 3 connectivity across resources
Deep programmability in both computing power and network itself
Easy experiments reproducibility to let you save and share your experiment setup (Rspec)
Provide network monitoring and management tool for your own resource slice
Cons:
Limited resources on a specific GENI site (ex: small server rack and recourses hogging by others)
GENI sites regular maintenance can cause delay of your experiments
Sudden server outage can cause the total loss of reserved experiment resources (Computing and network links)!!!
Layer 3 stitching between GENI sites are not stable and with less bandwidth (<100Mbps)
Notes: https://www.geni.net/about-geni/what-is-geni/
GENI might be right for you if your experiment requires:
A large-scale experiment infrastructure. GENI can potentially provide you with more resources than is typically found in any one laboratory. GENI gives you access to hundreds of widely distributed resources including compute resources such as virtual machines and “bare-machines”, and network resources such as links, switches and WiMax base stations.
Non-IP connectivity across resources. GENI allows you to set up Layer 2 connections between compute resources and run your own Layer 3 and above protocols connecting these resources.
Deep programmability. With GENI you can program not only the end hosts of your experimental network but also the switches in the core of your network. This allows you to experiment with novel network layer protocols or with novel IP-routing algorithms.
Reproducibility. You can get exclusive access to certain GENI resources including CPU resources and network resources. This gives you control over your experiment’s environment and hence the ability for you and others to repeat experiments under identical or very similar conditions.
Instrumentation and measurement tools. GENI has instrumentation and measurement systems that provide probes for active and passive measurements, measurement data storage and tools for visualizing and analyzing measurement data.

## Slide 9: Case Study 2 Dynamic Network Reconfiguration on the GENI[3]
In order to run the dynamic network reconfiguration on GENI
  Configure each VM in the topology to be a virtual router
    Install XORP, creating OSPF configuration file (GpENI-VINI by default provides this)
  Install iperf
  Execute the experimental flows and collecting data

## Slide 10: Case Study 3 Evaluating QoE of Video Streaming on the GENI Testbed[4,5]
Segment Aware Rate Adaptation (SARA)[3,4] algorithm
  Current algorithms assume the segment sizes are constant (average segment size)
  The size of the HTTP objects affects the throughput
Evaluating the improvement in QoE of video streams using SARA
QoE Metrics used for evaluation
  Bitrate switching
  Video Quality
  Convergence: Number of segments downloaded before reaching best bitrate

## Slide 11: One of the metrics: Bitrate Switching Events (Available bandwidth = 0.5Mbps)
Short Interruptions
Long Interruptions
Note: This high variance was observed for the Valkaama video and this is caused by the higher fluctuations
in segment sizes for this particular video.

## Slide 12: Ease due to Automation
GENI topology.xml file to setup the network
Astream Client code on Github
Open Source video files:
  ITEC DASH Dataset (http://www-itec.uni-klu.ac.at/ftp/datasets/
Open-source libraries to fro bandwidth variation
  Traffic Control (tc)

## Slide 13: Variation due to replication for Video QoE over GENI
From one run to another: the client’s “observation” varies partly due to the result of the RTT variation on the underlying infrastructure.
High variance was observed for the Valkaama video: this was further caused by the higher fluctuations in segment sizes for this particular video,

## Slide 14: Case Study 4 Hadoop Cluster Deployment on GENI[6]
(part of work on Application-Aware Networking (AAN) over SDN approach; see [6] for more details)
Notes: GENI Racks
http://groups.geni.net/geni/wiki/GENIRacksHome

## Slide 15
Hadoop MapReduce (M/R)Architecture Overview
HDFS
SlaveNodes
JobTracker
HDFS
SlaveNodes
Reduce 1
Reduce 2
TaskTrackers
Block 1
Block 2
Block 3
Block 4
Map1
Map2
Map3
Map4
HDFS
shuffle
NameNode
SlaveNodes
NameNode

## Slide 16: Hadoop over GENI: Experience
Challenges:
Most of the regular GENI nodes (InstaGENI) don not have enough computing power to run CPU-/memory-intensive M/R jobs, such as PageRanking and TeraSort. That causes us to give up around 2/3 of total experiments.
The default disk capacity is ~10GB.
It is difficult to get more than 20 nodes on one GEII sites and Layer 3 connection is not stable at that time.
Server Failure can cause the total resources loss (InstaGENI is more stable than ExoGENI)
Result variation in Replicated Runs:
  By nature, each Hadoop job run is a discrete and independent experiment. There is no way to get the exact same test results in terms of job running time, memory usage and etc.
  In other words, Scheduling algorithm, CPU and Memory usage, replication node selection even for the same job will be different.
Advantages
Hadoop Cluster Topology can be easily (re-)deployed (with customized scripts)
Network behaviors such as network bandwidth in your own slice are controllable.
It is possible to control multiple nodes at the same time either with scripting and web Portal
It allows Software-defined networking deployment using OpenFlow protocol and openVSwitch (OVS)
GENI google user group can help you with pretty much anything (if you still have the resource up and running).

## Slide 17: Hadoop over GENI
We conduct 330 tests for 11 setups and took 95% percentage interval for the all of the showing result
Hadoop Cluster Hardware Resource for various M/R jobs:
  CPU Usage
  Memory Usage
HiBench MapReduce Job Run time
Intermedia Data Transfer Capture
Critical Data Flow Identification
SDN Control Traffic Cost

## Slide 18: Hardware usage: CPU and Memory

## Slide 19: Job Run Time and Intermedia Data

## Slide 20: Hadoop Cluster Deployment Example and Some Test Results
Notes: We conduct 330 tests for 11 setups and took 95% percentage interval for the all of the showing result
Hadoop Cluster Hardware Resource for various M/R jobs:
  CPU Usage
  Memory Usage
HiBench MapReduce Job Run time
Intermedia Data Transfer Capture
Critical Data Flow Identification
SDN Control Traffic Cost

## Slide 21: Lesson Learned: Set up Automation
Test-automate-test-save cycle[1]
Procedures for building experiments on a public shared testbed[1]

## Slide 22: Statistical Validity and Robustness for Reproducibility
Important to run multiple replications
  - Results differ due a variety of reasons from one run to another
    Some times, testbeds are virtual networks themselves – conditions differ
Importance to report on Confidence Interval!
“Fundamental principles of statistical design” [7]
  Fundamental principle 1: “Science is knowledge obtained by repeated experiment or observation: if n = 1, it is not science, as it has not been shown to be reproducible. You need a random sample of independent measurements.”
  Fundamental principle 4: “Although replicates cannot support inference on the main experimental questions, they do provide important quality controls of the conduct of experiments.”

## Slide 23: References
[1] S. Edward, X. Liu, N. Riga, Creating Repeatable Computer Science and Networking Experiments on Shared, Public Testbeds, ACM SIGOPS Operating Systems Review, 2015.
[2] X. Liu, P. Juluri, D. Medhi, An Experimental Study on Dynamic Network Reconfiguration in a Virtualized Network Environment Using Autonomic Management, Proc of 2013 IFIP/IEEE Integrated Network Management Symposium (IM), Ghent, Belgium, 2013.
[3] Xuan Liu, Nicky Riga, Deep Medhi "Design of a software-defined resilient virtualized networking environment." Proc. 2015 11th International Conference on the Design of Reliable Communication Networks (DRCN),. 2015.
[4] Juluri, Parikshit, Venkatesh Tamarapalli, and Deep Medhi. "SARA: Segment aware rate adaptation algorithm for dynamic adaptive streaming over HTTP." Proc. of 2015 IEEE International Conference on Communication Workshops (ICCW), London, UK, 2015.
[5] Parikshit Juluri, Venkatesh Tamarapalli, and Deep Medhi. "QoE management in DASH systems using the segment aware rate adaptation algorithm." Proc. of 2016 IEEE/IFIP Network Operations and Management Symposium (NOMS), Istanbul, Turkey, April 2016.
[6] Shuai Zhao and Deep Medhi. "Application-Aware Network Design for Hadoop MapReduce Optimization Using Software-Defined Networking." IEEE Transactions on Network and Service Management, 2017, available online July 2017: DOI: 10.1109/TNSM.2017.2728519
[7] David L. Vaux, Fiona Fidler & Geoff Cumming, "Replicates and repeats - what is the difference and is it significant?" EMBO reports, vol. 13, No. 4. 2012

## Slide 24: Machine Learning in Communication Networks

## Slide 25: Broad Areas
Network Analytics
Network Applications
Network Automations

## Slide 26: Network analytics
  Machine learning, data mining and big data analytics in networking
  Data mining, statistical modeling, and machine learning for network management
  Network problem diagnosis through machine learning
Source: JSAC CfP (for this and the next two slides)

## Slide 27: Network Applications
  Network architecture and optimization for AI/ML applications at scale
  Machine learning for multimedia networking
  Resource allocation for shared/virtualized networks using machine learning
  Protocol design and optimization using machine learning
  AI/ML for wireless network resource management and medium access control
  Energy-efficient network operations via AI/ML algorithms
  Reliability, robustness and safety for networks optimized and operated based on AI techniques
  Security concepts for networks optimized and operated based on AI/ML concepts
  AI/ML Algorithms for network security
  Open-source networking optimization software for AI/ML applications

## Slide 28: Network Automation
  Deep learning and reinforcement learning in network control & management
  Proactive network monitoring architecture
  Self-learning and adaptive networking protocols and algorithms
  Predictive and self-aware networking maintenance
  Open-source AI algorithms and software for networking